## Slide 1: Deep learning proxy of reservoir simulation
ACSE 9 - Independent Research Project
Raha Moosavi
Supervisors : Dr Daniel Busby, Dr Yves Leory

## Slide 2: Problem statement
Deep learning proxy of reservoir simulation
Most simulation software using Numerical simulation like FD,FE &FV
Need to increase discretization grids to increase accuracy
History-matchings need several simulation runs
Next

## Slide 3
Deep learning proxy of reservoir simulation
Resource : History Matching In Parallel Computational Environments
Chart: No. of grid blocks
| 48 | 4800 | 19200 | 76800
No. of grid blocks | 4 | 21 | 76 | 530
Elapsed Time for Simulation In Sec.

## Slide 4
Deep learning proxy of reservoir simulation
Resource : History Matching In Parallel Computational Environments
Chart: Simulation Runs
| 5 | 12 | 21 | 28 | 32 | 35 | 36 | 38 | 45 | 46 | 47 | 53 | 56
Objective function | 90 | 100 | 20 | 40 | 38 | 2.5 | 1 | 0.8 | 6 | 1.8 | 1.6 | 3 | 0.8
Objective function

## Slide 5: Objectives and Motivation
Applying deep neural networks to simulating reservoir pressure and saturation by feeding geological parameter map (permeability) to network.
Assessing the surrogate model performance in simulating reservoir properties (pressure and saturation).
Put the performance of the proposed method in relation to surrogate models using shallow networks.
Deep learning proxy of reservoir simulation

## Slide 6: Synthetic dataset
3000 permeability map (Channelized facial map)
Simulating corresponding pressure and saturation
Simulating for 61 time step using Intersect
2250 training /750 Testing
Deep learning proxy of reservoir simulation

## Slide 7: Data preparation
Permeability and saturation are between 0 & 1.
Pressure is in wide range.
This normalization improves the model accuracy for pressure prediction.
Permeability map and its corresponding pressure and saturation
Deep learning proxy of reservoir simulation

## Slide 8: Deep learning model
Input : Permeability map & initial saturation or pressure
U-Net (Encoder/decoder) model
Output : pressure or saturation
Deep learning proxy of reservoir simulation

## Slide 9: Deep learning model architecture
Recently used model: Residual Recurrent U-Net
Our propose model: Attention Residual Recurrent U-Net
Convolution block
Residual block
ConvLSTM
Attention block
Deconvolution block

## Slide 10: Model architecture
Deep learning proxy of reservoir simulation

## Slide 11: Result
Deep learning proxy of reservoir simulation

## Slide 12
Deep learning proxy of reservoir simulation
Chart: Mean relative error for different models
| Saturation | Pressure
RR U-Net | 1.1 | 1.6
A RR U-Net | 0.9 | 1.4
Previous U-Net | 2.8 | 1.9
Model accuracy improvement :
Saturation: 1.9%
Pressure: 0.5%

## Slide 13: Future work
Some issues that can be investigated in future works:
Relative error increase with increasing time steps.
Training time increased with increasing no. of timesteps exponentially.
Number of required epochs to reach convergence.
Applying A RR U-NET model to 3D problem.
2021/09/10
Deep learning proxy of reservoir simulation
Next

## Slide 14: Relative error versus production time
Pressure
Saturation

## Slide 15
Chart: Training time VS No. of timesteps
| 10 | 16 | 20 | 30 | 60
Minutes/epochs | 1 | 7 | 25 | 55 | 180
Deep learning proxy of reservoir simulation
Next

## Slide 16: Acknowledgment
Dr. Daniel Busby
Dr. Yves Leory
PhD Students in TotalEnergies
Imperial College London
TotalEnergies
Any Questions?